EE5806: DSP Lab
Name: Shantanu Yadav
Roll.No: EE20MTECH12001
Assignment 4: Pseudo Code for BER Analysis of OFDM system	in AWGN channel

for Eb/N0 = 0:10 dB
SNR_lin=Es/N0 =1
sd=sqrt(Es/(2*SNR_lin)
N=1000
for iter = 1: N
1.	bit generation with uniform distribution
2.	digital modulation, mapping to symbol (BPSK/QPSK)
%OFDM Transmitter
3.	Reshape modulated symbols, Serial to Parallel Conversion
4.	Take N-IDFT (256 points) of BPSK/QPSK sequence to	generate OFDM
5.	Reshape for Parallel to Serial Conversion
6.	Insert cyclic prefix of length L (=32) (Take 32 samples	from	the end of OFDM sequence and append it to the	beginning of	sequence) to avoid Inter-symbol	Interference.
%Transmit OFDM symbols through AWGN channel
7.	Add AWGN
%OFDM Receiver
8.	Remove cyclic prefix
9.	Reshape for Serial to Parallel Conversion
10.	Take N-DFT (256 points)
11.	Reshape for Parallel to Serial Conversion
%Received symbols
12.	ML detector
13.	estimate bits using ML criteria.
14.	find no. of symbols in error.
15.	find no. of bits in error
end
BER(Eb/N0) = no. of bits in error/total no. of bits
end
Plot BER vs SNR(Eb/N0)